## Slide 1: Describing mechanisms
Material taken from EL2710: technical & scientific writing: teacher’s guide

## Slide 2: What is a mechanism?
A mechanism is any system of parts that operates in a definable way.
Anything that has a specific function can be called a mechanism.
It helps to know how things are constructed in order to clearly understand how they work.
The principles of description can usefully be applied to such diverse items as a fuel-injection system, diode, arch, bridge, mechanical pencil, gate valve, and innumerable other mechanisms in all technical areas.

## Slide 3: General guidelines for descriptions
Communicate clearly to inform an uninformed reader
Be thoroughly familiar with the mechanism. If possible, take it apart and examine it closely.
Do NOT become a victim of your own knowledge. Things that seem obvious to you, but crucial to the reader's understanding, can easily be overlooked.
Use visuals which can reinforce the description of a complex mechanism - they do not speak for themselves; they should never stand alone.
Visuals should be reserved for occasions when they will assist the effort to communicate.
The type of visuals you select depends upon the mechanism and the reader. A cross-sectional drawing may be better than an exploded view for clarifying a device.

## Slide 4: Outline for describing a mechanism
Introduction
  Definition and purpose of mechanism
  Overall appearance
  Identification of main parts
Description
  Part (Component) One
    Definition and purpose
    Appearance
      Size
      Shape
      Material
      Location and method of attachment
  C. etc.-Description of other parts

## Slide 5: Introduction
Provide an overview by defining the mechanism and its purpose, describing the mechanism's general appearance, and naming its main parts.
An effective introduction sends the reader into the body of the paper, the part-by-part description, with enough general information for him to be able to grasp the specifics of the mechanism.

## Slide 6: Introduction – Definition & Purpose
The uninformed reader needs a formal sentence definition.
For a reader who is familiar with the mechanism's general class, a more informal definition, emphasizing the differentia, may be sufficient.
Sometimes the definition adequately explains what the mechanism does, but an explicit statement of purpose often requires an additional sentence.
For example, to say that an air conditioner cools a room is to give the reader little information; a breeze through an open window does much the same thing. A clear explanation of the purpose of an air conditioner involves such things as circulation, filtration, and dehumidification.

## Slide 7: Introduction – overall appearance
In this section, state the dimensions and shape of the entire mechanism to give the reader a point of departure.
Along with the statement, a drawing with the main parts labelled can assist both an informed and uninformed reader, as a glance at any good manual will indicate.
If an illustration cannot be included, help the reader by comparing the overall mechanism to something he is better acquainted with.
For example, pointing out the similarity of a dune buggy to a jeep takes advantage of the reader's familiarity with the more common mechanism.

## Slide 8: Introduction – identification of main parts
The part-by-part description in the body of the report is organized according to the main parts identified in the introduction.
This approach allows the reader to assimilate the description bit by bit.
All mechanisms lend themselves to logical analysis, so breaking them into their main parts causes few problems.
For example, if you were describing a pencil sharpener, you would probably work from exterior to interior: the exterior casing; next, the frame; then, the cranking mechanism; and finally, the gear mechanism, which rests entirely in the interior.
As you identify the mechanism's main parts, list them in the order they will be described in the body so the reader knows exactly what to expect in the rest of the report.

## Slide 9: Introduction – description
In outline form, the detailed description of a part looks difficult, but once you actually start describing, things will fall into place
A single paragraph usually suffices for each part.
Use the "Definition and purpose" of the part, stated informally, as the topic sentence for each paragraph. When necessary, include a drawing of a complex part to reinforce its detailed description.
After you have written a topic sentence, you must consider 5 elements: size, shape, material, location, and method of attachment.
After describing the first main part of a mechanism, follow the same procedure for the remaining parts. A mechanism is the sum of its parts, and detailed descriptions of each add up to a detailed description of the entire mechanism. No conclusion is required.

## Slide 10: Example: Description of the gear system of a pencil sharpener
One of the four main parts of a pencil sharpener, the description of its gear system contains all 5 elements previously mentioned.
  The gear system consists mainly of three gears and two cylinders, all made of steel. The two identical cylinders are 1 inch in diameter and 1½ inches long (Fig 1). Each has 17 spiral edges which perform the cutting operation on the pencil. In order to sharpen the pencil to a 15-degree cone, each cylinder is held at a 7 ½ degree angle by a shaft which is crewed through a cranking mechanism (not shown). At one end of the cylinders are small gears with 9 teeth each. These teeth mesh with 22 teeth inside a stationary main gear 1 3/8 inches in diameter which is welded to a frame. The three gears form what is called a planetary gear system.

## Slide 11: Example continued
Size
In the example above, the sizes of the three main gears are stated. If several more dimensions were needed, the smaller ones could be placed on the drawing to avoid cluttering the text, which would then include only overall dimensions.
Depending on the purpose of the description, writers in industry provide either extremely thorough dimensions or, as in the example above, just enough dimensions to give the reader a perspective of the part.
Shape
In the description of the pencil sharpener's gear system, the words cylinder and gear, which indicate roundness, clarify the shape of the parts. Many times a simple analogy, comparing the part to a letter of the alphabet (A, C, L, T, U, among others) adequately suggests its shape.
Material
All the subparts of the gear system are made of the same material (steel). If an entire mechanism consists of only one material, you can state this in the introduction to avoid bothering with it in the detailed description.

## Slide 12: Example continued
Location and Method of Attachment
Location and method of attachment refer to the position of the subparts in relation to each other.
To clarify these relationships, you must examine the main part and determine a logical approach to describing its subparts.
The gear system's subparts are described in an order which reinforces their relationship to each other. Working essentially from left to right, the writer describes cylinders and their position in reference to each other, states how they connect to the cranking mechanism, how the gears mesh with the main gear, and how the main gear attaches to the frame.